## Slide 1
SLAM 的整体流程
观测 → 前端约束 → 后端优化 → 地图更新；地图继续约束下一帧定位
地图 / 局部结构为下一帧匹配提供约束
传感器观测
LiDAR / 相机 / 深度
IMU / 轮速等运动信息
按系统配置选择
预处理
时间同步与外参
去畸变 / 有效值检查
特征及可靠性筛选
前端：跟踪与关联
帧间 / 帧地图匹配
运动初值与相对约束
关键帧选择
后端：联合估计
融合观测与运动约束
优化位姿 / 偏置等
可含地图变量
地图融合与更新
用估计位姿融合观测
静态结构与变化管理
局部 / 全局地图
位姿影响地图，地图影响后续位姿。
误差会沿这个反馈关系传播。
输出 ① 位姿 / 轨迹
实时跟踪 + 后端校正
回环检测与验证
历史关键帧
几何一致性约束
输出 ② 环境地图
点云 / 栅格 / 特征等
本轮实验：给定建图位姿 A → 清理并冻结地图 → 独立扫描 B 定位；该对照用于隔离地图因素。
通用功能流程；各 SLAM 系统的模块划分和状态变量可不同。

## Slide 2
影响鲁棒定位与 SLAM 的因素和实例
读法：因素 → 典型实例 → 影响机制；右侧虚线框用于插入实测图。
F01 采样与可见性
例：远处细柱 / 大面积遮挡
稀疏、低重叠 → 匹配与建图约束不足
F01 配图位
稀疏 / 遮挡
F02 运动与扫描畸变
例：快速转弯 / 振动 / 轮胎打滑
扫描拉弯或运动先验失真 → 错误对齐
F02 配图位
转弯 / 墙面
F03 时间与空间标定
例：LiDAR–IMU 时间差 / 外参偏差
跨传感器错位 → 双墙与位姿偏差
F03 配图位
错位 / 双墙
F04 动态物体与持久变化
例：行人经过 / 停车 / 桌椅搬动
残影、遮挡或地图过期 → 误匹配
F04 配图位
动态残影
F05 材质与成像条件
例：镜面 / 玻璃 / 深度相机强光
虚假点、穿透或缺测 → 伪结构与空洞
F05 配图位
镜面 / 异常点
F06 几何与外观退化
例：平行长走廊 / 白墙 / 重复门
方向约束弱或易混淆 → 漂移 / 误关联
F06 配图位
长走廊
F07 位姿漂移与错误回环
例：累计偏航 / 相似走廊误闭环
地图错层或拉扯 → 后续定位被误导
F07 配图位
轨迹 / 错层
F08 地图表示与实时预算
例：体素过粗 / 过度滤波 / 处理积压
细节丢失、延迟 → 有效约束减少
F08 配图位
细节 / 延迟
静态不等于可信；干净不等于约束充分；未观测不等于自由空间。各因素可同时出现。

## Slide 3
The SLAM workflow
Observations → front-end constraints → optimization → map update → next-frame tracking
Map / local structure constrains the next match
Sensor input
LiDAR / vision / depth
IMU / wheel motion
As configured
Preprocessing
Time / extrinsics
Deskew / validity
Features / reliability
Front end
Frame / map matching
Relative motion factors
Keyframes
Back end
Fuse sensor factors
Pose / bias optimization
Map variables if used
Map update
Fuse scans with poses
Static / change updates
Local / global maps
Pose affects the map.
The map affects later pose.
Errors can propagate between them.
Output 1 · Pose / path
Tracked + optimized
Loop detection
Keyframe retrieval
Geometry validation
Output 2 · Map
Points / grids / features
Current experiment: supplied mapping poses A → clean and freeze map → localize independent scans B.
Functional overview; module boundaries and estimated variables vary across SLAM systems.

## Slide 4
Factors and examples affecting robust localization and SLAM
Read each entry as factor → example → mechanism. Dashed slots are reserved for your images.
F01 Sampling and visibility
E.g. distant poles / heavy occlusion
Sparse, low-overlap support weakens matching.
F01 IMAGE SLOT
Sparse scan / occluded scene
F02 Motion and scan distortion
E.g. fast turns / vibration / wheel slip
Warped scans or a biased motion prior misalign.
F02 IMAGE SLOT
Turning scan / warped wall
F03 Timing and calibration
E.g. LiDAR–IMU time / extrinsic offsets
Cross-sensor misalignment creates double walls.
F03 IMAGE SLOT
Time offset / double wall
F04 Dynamics and lasting change
E.g. walking / parking / moved furniture
Ghosts, occlusion or stale maps mislead matching.
F04 IMAGE SLOT
Ghosts / changed scene
F05 Materials and imaging
E.g. mirrors / glass / depth in strong light
False or missing returns create wrong geometry.
F05 IMAGE SLOT
Mirror / anomalous returns
F06 Geometry and appearance
E.g. parallel corridor / blank or repeated walls
Weak or ambiguous support causes drift / aliasing.
F06 IMAGE SLOT
Corridor / repeated structures
F07 Pose drift and false loops
E.g. yaw drift / similar corridors closed wrongly
Misplaced or warped maps corrupt later tracking.
F07 IMAGE SLOT
Trajectory / misaligned map
F08 Map representation and compute
E.g. coarse voxels / heavy filtering / backlog
Lost detail and stale updates reduce useful support.
F08 IMAGE SLOT
Detail loss / processing delay
Static ≠ reliable; clean ≠ sufficiently constrained; unobserved ≠ free. Factors can co-occur.